## Slide 1
REVIEW 1 — RESEARCH PROGRESS
An Explainable AI-Based Framework for Water Quality Index Prediction and Decision Support Using Machine Learning and TabNet
Submitted by Student Names:
Chintakayala Karthikeya Ameer Roshan Shaik
Shaik Abdul Samad Desam Pranay Kumar Reddy Roll Numbers:
23BCE9594 23BCE9533
23BCE7692 23BCE8722
Department of Computer Science & Engineering VIT-AP University
Under the Guidance of Prof. Balusa Bhanu Chander
Academic Year: 2026–27

## Slide 2
PROBLEM STATEMENT
Why Water Quality Index?
River water quality is governed by multiple physical and chemical parameters. Assessing each parameter individually across hundreds of stations and decades of data makes overall condition difficult to interpret.
A Water Quality Index (WQI) converts multiple measurements into a single interpretable score — providing a summarised condition and a target for machine-learning prediction.

## Slide 3
RESEARCH DESIGN
Research Gap and Objectives
Research Gap
Long-term datasets contain heterogeneous observations across stations and years
Individual parameters are difficult to interpret as one overall condition
Prediction alone does not explain which parameters influence the result
A link between prediction, explainability, and decision support is needed
Objectives
Prepare and quality-control the NIEA river water-quality dataset
Construct a CCME-WQI from selected parameters
Develop ML and DL models for WQI prediction
Compare Random Forest, XGBoost, CatBoost, and TabNet
Use SHAP to explain model predictions
Connect prediction and explanation to recommendation-oriented decision support

## Slide 4
DATASET
Dataset and Initial Data Understanding
178,680
Raw Observations
40
Raw Variables
1,311
Monitoring Stations
34
Years of Coverage
1990–2024
The raw NIEA dataset contains long-term river water-quality observations collected across multiple monitoring stations in Northern Ireland. Initial inspection examined data types, temporal coverage, parameter availability, missing values, quality indicators, and measurement ranges.
178,680 Records
Individual measurement entries
1,311 Stations
Coverage 1990–2024
NIEA Raw Dataset
Long-term river observations
40 Variables
Water-quality parameters

## Slide 5
DATA PROCESSING
Data Preprocessing and Quality Control
Completed preprocessing steps:
Selected relevant water-quality parameters
Extracted Year from monitoring dates
Standardised the working dataset structure
Examined missing values, negative values, and extreme observations
Investigated quality flags
Prepared station-year groups
Extreme values were investigated rather than automatically removed — genuine environmental events may produce unusually high measurements.
Missing Value Rates
Raw Dataset
178,680 × 40
↓ Preprocessing
Data cleaning & selection
Core Dataset
175,615 × 13

## Slide 6
AGGREGATION
Station-Year Aggregation
Raw Observations
178,680 total records
Station-Year Groups
15,502 aggregated groups
Group by StationCode & Year
Create station-year units
Each station-year group serves as the unit of annual water-quality assessment for WQI construction.
15,502
Station-year groups
11.33
Mean observations per group
12
Median observations (typical)
1–28
Range of observations per group
The raw dataset contains repeated observations from the same station across different dates. To create a consistent annual assessment unit, observations were grouped by StationCode and Year.

## Slide 7
METHODOLOGY
CCME-WQI Construction
Five parameters were selected based on availability in the processed NIEA dataset and compatibility with the CCME-WQI formulation:
BOD (Biochemical Oxygen Demand)
Ammonia-N, Nitrite-N, Nitrate-N
pH
The CCME-WQI combines three components — Scope (F1), Frequency (F2), and Amplitude (F3) — into a single score from 0 to 100.
Formula: CCME-WQI = 100 − √(F1² + F2² + F3²) / 1.732

## Slide 8
RESULTS
Initial WQI Results and Validation
12,497
Final WQI Records
49.43
Mean WQI
46.66
Median WQI
0
Invalid Values
None outside 0–100
WQI values remained within the valid 0–100 range. The majority of station-year records were classified as Poor (5,691) or Marginal (5,044), while only 19 records were classified as Excellent.
These categories reflect calculated WQI values — not ML predictions. Predictive modelling is the next phase.

## Slide 9
FRAMEWORK
Overall Framework and Current Progress
✅ Completed — Review 1
01
NIEA Raw Dataset
02
Data Inspection
03
Preprocessing
04
Quality Control
05
Station-Year Aggregation
06
CCME-WQI Construction
07
WQI Validation
08
Final WQI Dataset
⏭ Next Phase
01
ML Dataset Preparation
02
Random Forest · XGBoost · CatBoost · TabNet
03
Model Evaluation (MAE, MSE, RMSE, R²)
04
SHAP Explainability
05
Water-Quality Interpretation
06
Recommendation Layer
07
Decision Support System

## Slide 10
SUMMARY
Conclusion and Next Phase
Completed
Long-term NIEA dataset successfully inspected and processed
175,615 observations prepared; 15,502 station-year groups identified
CCME-WQI successfully constructed and validated
12,497 valid station-year WQI records generated
Dataset and target are ready for predictive modelling
Next Phase
Prepare leakage-free ML dataset
Train and compare Random Forest, XGBoost, CatBoost, and TabNet
Evaluate using MAE, MSE, RMSE, and R²
Apply SHAP for explainability
Develop recommendation-oriented decision support
Current Status: Data processing and WQI construction completed. Predictive modelling and explainability are the next phase.